Hunter Douglas EOS® 500 Roller Blind

EOS® 500 S-Series

Brackets (5-410-models)

| 1 | Brand | Hunter Douglas |
| --- | --- | --- |
| 2 | System | Roller Blind EOS® 500 S 5-410 Series |

Fabric

| 3 | Fabric description |  |
| --- | --- | --- |
| 4 | Fabric color |  |
| 5 | Fabric properties | - Transparency / openness - Fenestration data - Fire resistance rating - Environmental requirements - Other |

Dimensions

| 6 | Width (mm) |  |
| --- | --- | --- |
| 7 | Height (mm) |  |
| 8 | Quantity (pcs) |  |

Model

| 9 | System brackets | Glass fibre reinforced PA brackets with 33, 38 or 46 mm projection (according to blind size and fabric type). Suitable for fixing to wall and ceiling with screws. White HD 0155 Grey HD 0952 Black HD 1858 Alternatively: Pearl chrome finished design brackets made of solid die cast zamac with 33, 38 or 46 mm projection for fitting to wall and ceiling with screws. Colour pearl chrome with black round inlay on side. |
| --- | --- | --- |
| 10 | System profile | Not applicable |
| 11 | Tube | Extruded aluminium, mill finish, alloy 6060-T66-EN755 Diameter internal Ø 31 mm or Ø 37 mm Wall thickness 1.1 or 1.6 mm according to fabric, blind size and operation, unless differently specified. |
| 12 | Bottom rail | - Oval shape 26 x 15 mm - Aluminium extrusion alloy 6060-T66-EN755 - Natural anodized aluminium or powdercoated black or white |
| 13 | Plastic parts | Colour coordinated miscellaneous UV-stable compounds according to: White HD 0155 Grey HD 0952 Black HD 1858 |

Operation

| 14 | Operation type | Model 5-411 Operation with stainless steel ball chain, left or right side Model 5-416 Electric operation with 24V motor and switch, remote or group control Motor left or right side |
| --- | --- | --- |
| 15 | Operation motor | Available motor types: Standard silent HunterDouglas® M25T motor (24V DC) Somfy LT28 (24V DC) on request |
| 16 | Motor controls | In accordance with customer specification |

Installation

| 17 | Installation brackets | Standard or design brackets as previously described fitted with screws provided |
| --- | --- | --- |
| 18 | Spring loaded bearing | Self lubricating spring loaded plastic bearing for easy installation and quick removal. Tube can be easily demounted with any bank card. |

Guiding (optional)

| 19 | Cable side guiding (recommended when ratio width:drop < 1:3) | Maintenance free spring loaded cable tensioner for permanent tension fitted with bracket High tensile UV stabilized plastic coated steel wire Ø 1.0 mm Sill or wall mounted plastic hold down bracket |
| --- | --- | --- |

Leveling (optional)

| 20 | Leveler | Tube leveling component integrated in design bracket to limit skewing or adjust lateral openings. Manual height adjustment of bearing side (+/- 4 mm) with Allen key. Available only with design brackets as extra option. |
| --- | --- | --- |

Rolling

| 21 | Rolling direction | Standard back rolling, alternatively front rolling |
| --- | --- | --- |