## LUXALON® EXTERIOR 185U CEILING SYSTEM

# PART 1: GENERAL

  - INTRODUCTION

Supply and fix Luxalon® exterior 185U ceiling system as manufactured by Hunter Douglas Architectural Products.

  - DESCRIPTION OF THE SYSTEM

The system will consist of box shaped linear panels fixed to an adjustable suspension system, which allows for individual panels to be removed by hand. The suspension system consists of a non-Luxalon® levelled rigid suspension structure. To prevent contact corrosion by applying dissimilar metals, each fixing of the carriers to the subconstruction must be made through the Luxalon® washer set.

# PART 2: PRODUCT

2.1 PANELS

185U, size 185 x 25 mm manufactured from 0.95 mm aluminium.

Panels to be manufactured from prepainted, stove enamelled aluminium, corrosion resistant alloy EN-AW-3005 or equivalent (according to EN 1396 and ECCA). Panels have al length of 	 mm (manufacturer availability 1000-6000 mm and on request 250-1000 mm and > 6000 mm). Panels to be coupled in longitudinal direction by means of panel splices.

2.2 SUSPENSION

Rows of 0.95 mm aluminium rollformed carriers shall be installed at 	 centre on centre by means of a levelled rigid suspension system of sufficient strength and rigidity to provide resistance to wind pressure/-suction at a distance of 	 , centre on centre. Carriers will be joined by means of carrier splices. Carriers provided with prongs to hold panels with a total module of 200 mm.

PART 3: ADDITIONAL SPECIFICATIONS

3.1 PERIMETER PROFILES

- Wall L-profile 45 x 18.5 mm made of 0.8 mm thick aluminium

- Wall W-profile 45 x 21 x 21 x 18.5 mm made of 0.8 mm thick aluminium

3.2 COATING

Architect will make a colour selection from the standard Hunter Douglas colour range for Luxalon® exterior 185U panels code no. 		 Or a special colour will be made to match.

The coating will consist of a tough and durable Luxacote® finish in a nominal thickness of approximately  20 microns, applied in a continuous coilcoating process ensuring a uniform coating.

Luxacote® finish guarantees optimum adhesion and excellent resistance to weathering.

3.3 INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications of shown on the drawings.