# LUXALON( CELL T15 SPECIFICATION

## PART 1: GENERAL

  - INTRODUCTION

Supply and fix Luxalon® Cell T15 Ceiling System as manufactured by Hunter Douglas Architectural Products.

  - DESCRIPTION OF THE SYSTEM

The system will consist of cell tiles integrating with a disguised suspension grid. Tiles formed by interlocking U-profiles; suspension grid formed by T-profiles. System to allow for easy placement and removal of the tiles.

## PART 2: PRODUCT

_________m2 Luxalon® Cell T15 Ceiling, tiles to be manufactured from prepainted,

stove enamelled aluminium material, alloy AA5050 or equal (according to EN 1396 and ECCA standards), thickness 0.35 mm to achieve a cell size of ____x____mm.

_________tiles of 600 x 1200 mm

_________tiles of 600 x   600 mm

All U-profiles to be 15 mm wide and 40 mm high. Each CellT15 tile to be provided with a 37 mm high flat edge strip in the same colour as the Cell T15 tile in order to hide the supporting T-grid.

The U-profiles of the Cell Tiles are to feature cut-outs at their ends that allow for the tile to self-align and fit flush with the 15 mm T-grid. When incorporated into the suspension grid, the tiles shall fully integrate in the cell ceiling.

The Cell Tiles are to be installed in the suspension grid without the use of further fixing materials.

The suspension grid consists of commercially available 15 mm wide T-profiles. Colour of the T-grid to match the colour of the Luxalon® Cell T15 Tiles.

Further dimension to be as specified for Luxalon® Cell T15 ceiling.

## PART 3: ADDITIONAL SPECIFICATIONS

  - PERIMETER PROFILES

L-profiles (25 x 50 mm) made of 0.5 mm thick aluminium, for wall-to-wall installation.

The perimeter profiles to have the same colour coating quality as the Luxalon( Cell T15 Ceiling on all visually exposed sides.

  - COATING

Architect will make a colour selection from the standard Hunter Douglas colour range for Luxalon® Cell T15 code no. ______special colour will be made to match_____.

The coating will consist of a tough and durable 2-layer polyester finish in nominal thickness of 20 microns, applied in a continuous coil-coating process ensuring uniform coating and absolute adhesion.

  - INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.

  - SUBSTITUTIONS

Ceiling installers wishing to submit proposals on systems other then the Luxalon( Cell T15 Ceiling System shall, at least 10 days in advance of the bid date, submit to the architect complete descriptive information of the total system concept and performance data tests made as a system. In addition include a list of similar installations of the proposed substitution. If approval is made an addendum will be issued enumerating such approved system as herein set forth.