# Luxalon( Stretch Metal Lay-on Plank System specification

## PART 1. GENERAL

    - INTRODUCTION

Supply and fix Luxalon( Stretch Metal Lay-on Plank System as manufactured by Hunter Douglas Architectural Products.

    - DESCRIPTION OF THE SYSTEM

The system will consist of Bandraster profiles installed uni directionally or in a grid pattern or Wall L-profiles. The panels are layed on the Bandraster or Wall profiles.

## PART 2. PRODUCT

________m2 Luxalon( Stretch Metal Lay-on Plank Ceiling consisting of:

  - PANELS:

Panels to be set from 1.0  mm stretch metal steel sheets.

The stretch metal Lay-on planks are 300, 400 or 500 mm wide panels to feature square edges to form visually closed joints or a flushed joint.

Panels to be manufactured from post painted steel stretch metal sheet. Panels to have a length of______ mm. (manufacturer availability 1500 mm without support profile, 2400mm with a welded support profile or 2800 mm with a welded C-profile).

  - SUSPENSION:

Consists of Bandraster profiles or Wall L profiles manufactured of galvanized steel.

Bandraster of Wall L profiles will be finished in a requested RAL colour.

## PART 3: ADDITIONAL SPECIFICATIONS

  - PERIMETER PROFILES

- L-profile 25  x  25 mm made of 1.5 mm thick steel

- W-profile 25 x 25 x 8 mm made of 1.5  thick steel

- F-profile, 35 x 40 mm, made of 1.5 thick steel

- L profile angled, 40 x 30 mm(12° angle), made of 1.5 thick steel

  - Mesh types

Manufacturer shall supply all Stretch Metal Lay-on planks with the following steel  mesh types:

- LD6, open area 23 %

- LS6, open area 38 %

- LS8, open area 62 %

- LS12, oper area 72 %

  - ACOUSTICS

Manufacturer shall supply acoustic pads white/black to put on top of the stretch metal tiles,  thickness___mm density____kg/m3 and of a size completely fill the tile.

  - COATING

Architect will make a colour selection from the RAL colour range collection for Luxalon( Stretch Metal Lay-on plank system RAL code no._______or a special colour will be made to match.

The coating will consist of a tough and durable polyester powder coating finish, electro statically applied into electro-galvanized steel, phosphatised and chemically treated according to high industrial standards (DIN 1541/ TAIM standards).

  - INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.

  - SUBSTITUTIONS

Ceiling installers wishing to submit proposals on systems other than the Luxalon Stretch Metal C-Grid System shall, at least 20 days in advance of the bid date, submit to the architect complete descriptive information of the total system concept and performance data tests made as a system . In addition include a list of similar installations of the proposed substitution. If approval is made an addendum will be issued enumerating such approved system as herein set forth.