## PART 1: GENERAL

1.1 INTRODUCTION

Supply and fix Luxalon® Unigrid Ceiling System as manufactured by Hunter Douglas Architectural Products.

1.2 DESCRIPTION OF THE SYSTEM

The system will consist of Luxalon® Unigrid Ceiling tiles of dimension 600 x 600 or 600 x 1200 mm

The module will be _________ x _________ mm

The height will be __________________ mm

The type shall be:

[ ] Wave

[ ] Focal

[ ] Crête

[ ] Piquée (perforated)

## PART 2: PRODUCT

2.1 PANELS

Ceiling of _________m2 Luxalon® Unigrid Ceiling to be manufactured from pre-painted, stove enamelled aluminium material, alloy AA5050 or equal (according to EN 1396 and ECCA standards), thickness 0.6 mm.

2.2 SUSPENSION

A standard grid shall be installed in order to receive the panels.

The grid shall be of type:

1. T24 lay-on, height 0

2. T24 lay-in

3. T24 lay in concealed

## PART 3: ADDITIONAL SPECIFICATIONS

3.1 COATING

Architect will make a colour selection from the standard Hunter Douglas colour range for Luxalon® Unigrid code no. _________ or a special colour will be made to match _________.

The coating will consist of a tough and durable 2-layer polyester finish in nominal thickness of 20 microns, applied in a continuous coil-coating process ensuring uniform coating and absolute adhesion.

3.3 INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.

3.4 SUBSTITUTIONS

Ceiling installers wishing Luxalon® Unigrid Ceiling System shall, at least 10 days in advance of the bid date, submit to the architect complete descriptive information of the total system concept and performance data tests made as a system. In addition, include a list of similar installations of the proposed substitution. If approval is made an addendum will be issued enumerating such approved system as herein set forth.