## PART 1: GENERAL

  - INTRODUCTION

Supply and fix Luxalon® 70U system as manufactured by Hunter Douglas Architectural Products.

  - DESCRIPTION OF THE SYSTEM

The system will consist of linear box shaped panels fixed to an adjustable suspension system which allows for individual panels to be removed by hand. System to feature open joints between the panels.

## PART 2: PRODUCT

_________m2 Luxalon( 70U ceiling, featuring a 30 mm joint and consisting of:

  - PANELS

Panels, 70 mm wide, 25 mm deep, to be roll formed from 0.8 mm thick stove enamelled aluminium strip or from 08. mm thick stove enamelled galvanised steel strip, plain. Optionally acoustic pads can be laid on the panels in order to improve acoustical performance.

- Aluminium panels to be manufactured from pre-painted, stove enamelled aluminium, alloy EN-AW-3005 or equivalent (according to EN 1396 and ECCA).

- Steel panels to be manufactured from pre-painted, stove enamelled steel.

Panels have a length of ______mm (manufacturer availability 1000-6000 mm and on request 250-1000 mm and > 6000 mm). Panels to be coupled in longitudinal  direction by means of panel splices.

  - SUSPENSION

Rows of 1.0 Fe/0.95 Alu roll formed carriers shall be installed at ______ centre on centre by means of adjustable suspensions, of suitable strength and rigidity to provide impact resistance if required, at a distance of _________, centre on centre. Carriers shall be joined by means of carrier splices. Carriers provided with prongs to hold panels in a standard module of 100 mm.

Fixing clips made of stove enamelled aluminium, clipped on to the panel carrier between the panels in order to secure the panels.

PART 3: ADDITIONAL SPECIFICATIONS

  - PERIMETER PROFILES

- Wall L-profile, 29.2 x 19.4 mm, made of 0.5 mm thick aluminium

- Wall L-profile, 45 x 18.5 mm, made of 0,8  mm thick steel or aluminium

- Wall W-profile, 45 x 21 x 21x 18.5 mm, made of 0.8 mm thick steel or aluminium

  - ACOUSTICS

The installer can place individually P.E. wrapped mineral wool pads on top of the panels.

  - COATING

Architect will make a colour selection from the standard Hunter Douglas colour range for Luxalon® 70U panels code no._________or a special colour will be made to match.

The coating will consist of a tough and durable polyester finish in nominal thickness of 20 microns, applied in a continuous coil-coating process ensuring uniform coating and absolute adhesion.

For exterior and swimming pool applications the Luxacote® finish is recommended. The Luxacote® coating will consist of a tough and durable 3-layer polyurethane finish in a nominal thickness of approximately 30 microns, applied in a continuous coil-coating process. The ‘Anorcoat’ pre-treatment, the primer, the colour coating and the transparent topcoat are fully integrated during this process.

  - INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.