## PART 1: GENERAL

  - INTRODUCTION

Supply and fix Luxalon Closed Ceiling System as manufactured by Hunter Douglas Architectural Products.

  - DESCRIPTION OF THE SYSTEM

The system will consist of longitudinal panels clipped on to the carriers. The panels abut each other with a narrow V-groove. Panels for different widths can be combined as required in the ceiling.

## PART 2: PRODUCT

_________m2 Luxalon( Multi-panel Closed Ceiling, consisting of:

  - PANELS

75C, manufactured from 0,5 mm AL, size 75 x 15,5 mm

150C, manufactured from 0,5 mm AL, size 150 x 15,5 mm

225C, manufactured from 0,6 mm AL, size 225 x 15,5 mm

Panels to be manufactured from pre-painted, stove enamelled, alloy HD5050 or

equal (according to EN 1396 and ECCA).

All panels to be securely clipped to carriers in accordance with manufacturers recommendations, Panels to be joined in length by using the relevant Luxalon( splice. Maximum panel length to be 6000 mm.

  - SUSPENSION

Rows of 0.6 Fe/0.95 Alu roll formed carriers shall be installed at __/__/__ centers by means of ______mm rod hangers fixed to the carrier by means of Luxalon universal suspension adjustment clips at a max, distance of __/__/__ mm, center to center.

Carriers with a max. length of 5000 mm to be coupled by means of carrier splices, automatically arranging for module continuation.

  - EXTERIOR APPLICATION

The Luxalon( Closed Ceiling System can also be used for exterior applications. For specification details concerning exterior applications contact your local Hunter Douglas office.

PART 3: ADDITIONAL SPECIFICATIONS

  - PERIMETER PROFILES

- Clip-on U-profile, 28.6x19x20 mm, made of 0.35 thick aluminium

- Wall L-profile, 29.2x19.4 mm, made of 0.5 mm thick aluminium

- Wall L-profile, 45x18.5 mm, made of 0,8  mm thick steel

- Wall W-profile, 45x21x21x18mm, made of 0.8 mm steel

  - PERFORATIONS

Manufacturer shall supply panels with following perforation specifications:

- 75C    :( 1.0 mm, ( 2 mm, open area 23%

- 150C  : ( 2.0 mm*, ( 5 mm, open area 16%

- 225C  : ( 1.5 mm, ( 3 mm, open area 23%

- 225C  : (  2.0 mm*, ( 5 mm, open area 16%

*( 2 mm perforation pattern of 150/225C shows an optical difference

Perforated 150/225C panels have a nominal plain border of approximately 9 mm

on the side for optimal flatness and stability. For 75C panels the plain border is 3

mm.

  - ACOUSTICS

Manufacturer shall supply acoustic non-woven tissue factory applied inside the panels or alternatively the installer can place individual wrapped mineral wool pads to the back of the installed ceiling panels.

  - COATING

Architect will make a colour selection from the standard Hunter Douglas colour range for Luxalon 75/150/225C panels code no._________or a special colour will be made to match___________.

The coating will consist of a tough and durable 2-layer polyester coil coating finish in thickness of 20 microns, applied in a continuous coil-coating process ensuring uniform coating and absolute adhesion.

3.5 INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.

  - SUBSTITUTIONS

Ceiling installers wishing to submit proposals on systems other than the Luxalon( Closed Ceiling, at least 10 days in advance of the bid date, submit to the architect complete descriptive information of the total system concept and performance data tests made as a system. In addition include a list of similar installations of the proposed substitution. If approval is made an addendum will be issued enumerating such approved system as herein set forth.