HunterDouglas®  Ultimate Screen Zip External Roller Blind

| 1 | Brand | Hunter Douglas |
| --- | --- | --- |
| 2 | System | External Roller Blind Ultimate Screen Zip |

Fabric

| 3 | Fabric description | - HunterDouglas® Sergé - HunterDouglas® Carré |
| --- | --- | --- |
| 4 | Fabric colour | HunterDouglas® Sergé 108101 F/B 108108 Uni 108118 F/B 118118 Uni 108112 F/B 112101 F/B 116101 F/B 116116 Uni 117101 F/B 117117 Uni HunterDouglas® Carré 101208 101212 101216 101217 108301 108311 108317 108318 118118 118508 118517 F/B = Front or Back |
| 5 | Fabric properties | - Transparency / openness Sergé is 3% and Carré is 5% - Material Sergé and Carré is 42% Glass + 58% PVC - Fire resistance rating: M1 (French Norm NF P92-503) B1 (German Norm DIN 4102) C-S3,d0 (European Norm NEN-EN 13501-1) - Weather resistant - Reinforced on side with a welded Zip |

Dimensions

| 6 | Width x Height (mm) | Box 100 max: 4000 x 2700 mm or 3000 x 3500 mm Box 125 max: 4300 x 3400 or 3000 x 5000 mm |
| --- | --- | --- |

Model

| 7 | Boxes | Several self-supporting head boxes made of extruded aluminium. The box is equipped with polypropylene profile to guide fabric inside. The boxes housing a complete mechanism and fabric. The boxes are designed to have a maintenance access. Security brackets are available. - Sizes: 100x100 mm 125x125 mm - Box shape: Square Chamfered - Endplates: made of a special die cast metal alloy and receive an anti- corrosive pretreatment before being RAL powder coated. When profiles are natural anodized the endplates are coated in RAL 9022. |
| --- | --- | --- |
| 8 | Side guiding | Aluminium side channel 37 x 38 mm to keep the fabric and head box in position. Fixation is ‘in recess’ or ‘on face’ of the window. Profile finishing: natural anodized or polyester powder coated. |
| 9 | Rolling tube | The tube is made of roll formed steel. Depending on blind sizes different tubes with throat to insert fabric are used: Ø 63 mm Ø 78 mm |
| 10 | Bottom bar | The color coordinated bottom bar of 22 x 48 mm is made of extruded aluminium and finished with a black and soft rubber seal. The fabric is attached to the bottom rail with a spline. The bottom bar is natural anodized or polyester powder coated. |

Operation

| 11 | Operation type | Standard motorized |
| --- | --- | --- |
| 12 | Operation side | Motor right or left |
| 13 | Operation motor | The boxes guide the motor cable to prevent to be cut by sharp edge of the zipper. Available motor types: M50S (standard) Quiet M50S 626 M50E Somfy LT 50 Somfy RTS Altus 50 Somfy IO RTS |
| 14 | Motor controls | In accordance with customer specification |

Installation

| 15 | Box installation | A patented design allows safe and easy frontal click fixation of the head box to pre-installed side guiding profiles. A stainless steel spring is added in the box to handle the box during installation. Stainless steel screws are added to secure the fixation. |
| --- | --- | --- |
| 16 | Installation specific brackets | Security brackets are necessary by box width > 3000 mm |
| 17 | Other installation brackets | Distance brackets on side guiding for face fixing or when front/contra rolling is added with a distance of min. 45 mm and max. 100 mm. |
| 18 | Channel/side guiding installation | There are two types of profiles; the based profile is fixed by screws on face or in recess and the cover profile is provided with a click system where screws are not visible. |

Rolling

| 19 | Rolling direction | Back rolling in all combinations and front rolling only in combination with square head boxes 100 x 100 mm. |
| --- | --- | --- |

Wind load

| 20 | Maximum wind load | Ultimate Screen Zip Roller Blinds are Class 3 products that can withstand wind speeds up to 16.8 m/s. |
| --- | --- | --- |